## Slide 1
Acoustic Mixed Reality Using
Extracted Clapping Sound as BRIR
◯S. Nishimura, A. Kawamura（Kyoto Sangyo University, Japan）
Proposed Method
Research Background
Experimental Setting
Real bird
Virtual monster
Real sound
Virtual 3D sound using BRIR
Monster really exists
on the right!
We assume clapping
sounds as BRIR
BRIR extraction
based on BRIR peak
Hallway (Room H)
Soundproof room (Room S)
clapped from some
directions by herself
BRIR is impulse response from acoustic source…
Waveform of Clapping sound
Acoustic MR：
Mixed sound of Real and Virtual 3D sounds with BRIR
: Integer to detect VF
: Threshold
*BRIR: Binaural Room Impulse Response
Questions.
Q1. Did you hear the sound coming from the direction where you clapped?
Q2. Did the sound seem to be coming within the room?
Subjects | 6 people
Binaural microphones | Roland CS-10EM
Location | Hallway(Room H) Soundproof(Room S)
*AMR(X) : 3D sound made by using BRIR detected in Room X
Results of subjective test for Q2
Results of subjective test for Q1
Sampling Freq. | 44.1kHz
D | 10
Th | 0.3
Length of BRIR | 22050 (0.5s)
Subject no.
Experimental Results
Rating | Meaning
5 4 3 2 1 | Excellent Good Average Poor Unacceptable
Lch
Rch
Binaural Microphones
BRIR peak detection